## Slide 1
Structured Programming Guidelines (just a few)
know the basic hardware/software basics
understand/define the problem
determine the solution
implement the solution
test the solution

## Slide 2
Programming Guidelines
know the hardware architecture – programmers model
data registers (ACCA, ACCB, ACCD)
address registers (IX, IX, SP)
control registers (CCR)
input/ouput registers (e.g. parallel port, serial port)
timers/accumulators
know the basics of assembly language
load and store
arithmatic operations
logic operations
shift and rotate
stack operations
clear and set
branches and jumps
compare

## Slide 3
Programming Guidelines
understand/define the problem (requirements definition)
user requirements: what does the user want?
functional requirements: what does it have to do?
performance requirements: how well/fast, etc does is have to do it
estimate CPU resources (memory, processing speed, support, availability…)
determine the solution (software design)
break the problem into smaller components
design a solution for each requirement
trace each designed solution back to a requirement
assess each solution for correctness: analytical, simulation
define interface between modules
do not write actual code during this phase (‘what if’ code is ok)

## Slide 4
Programming Guidelines
implement the solution (programming)
implement each aspect of design and test it individually (modules)
stubs: act like missing modules that you module must interface with
drivers: drives your software module as if it were part of a larger system
test the solution:
all testing should be peformed incrementally
module testing using stubs and drivers
interface testing
integration testing of multiple modules
final testing (e.g acceptance test/validation test) should never be performed by the developer
test planning should occur over the pror development cucle

## Slide 5
document
milestone
Requirements specification
Design
specification
1
2
n
Requirements
Phase
Design
Phase
Code
Phase
Test
Phase
preliminary
design
critical
design
verification test
validation test
code
1
2
n
test
readiness
system
definition
System
definition
1
2
n
Simplified Software Development Cycle

## Slide 6
Requirements specification
Design
specification
code
System
definition
Simplified Software Development Cycle – top down approach
water purification
1.1 water capacity
1.2 water flow rate
1.3 acceptable impurities
1.4. …..
….
1.3.1 initialize
1.3.2 measure impurities
1.3.3 check impurity level
1.3.4…
1.3.2.1 read A/D converter
1.3.2.2 scale A/D measurement
1.3.2.3 check for reading error
1.3.2.4…
code
unit 1
code
unit 2
code
unit 3
test planning

## Slide 7
Simplified Software Development Cycle – bottom up build
code
1.3.2.1 read A/D converter
1.3.2.2 scale A/D measurement
1.3.2.3 check for reading error
….
1.3.2.n…
code
unit 1
code
unit 2
code
unit n
Design specification
unit check out test
1
2
unit verification test
unit check out test
1
2
unit verification test
unit check out test
1
2
unit verification test
code unit integration
code
unit 1
code
unit 2
code
unit n
Requirements specification
….
1.3.1 initialize
1.3.2 measure impurities
1.3.3 check impurity level
1.3.4
…
integration check out test
1
2
validation test
1
2

## Slide 8
Programming Guidelines
what went wrong?
requirements are not well defined – requirements evolve over program development cycle. Requirements creep is the single biggest source of cost overun in programs and results in failed programs.
coding during design phase – blurs requirements-design mapping. Can cause design trace back to fail. Design does not trace back to requirements – unecessary code is written. Requirements may not be fullfilled.
often results when schedule is compressed – due to underbidding or requirements creep
inadequete testing
inadequete test planning due to compressed schedule
incomplete testing due to cost /schedule or awareness issues